Current research

Objectives

The primary and ultimate goal of this research program is to electrically monitor the real- time temporal conformational change of bio-molecules at the single molecule level. As discussed before, thanks to recent advances in nanoscale materials, ultra-sensitive electronic circuits can now be constructed in which the active component parts are comparable in size to individual biological entities. Research discussed in the "Prior Research" section of the proposal, together with what is described in subsequent sections give convincing evidence that using such circuits as an electronic interface, conformational change driven electronic signals may be studied in real time at the single-molecule scale. I propose to capture and characterize those signals as bio-molecules undergo specific, known fluctuations and interactions, such as DNA duplex formation, melting of the duplex, protein-protein binding and conformational changes of proteins.

Real-time signal acquisition and analysis may have significant impact the biological sciences for several reasons. First, the time scales for biological processes may be directly measured. The time for a protein to undergo conformational changes, or for a single-strand of DNA and its complement to form a duplex, could be directly measured. Secondly, the electronic data may be analyzed to seek electronic signatures specific to the dynamics of a particular process, as a specific biological process is most likely accompanied by specific electronic charge rearrangements which are sensed by the circuit. If the binding of different antigens to an antibody each results in a particular electronic signature, then the different antigens may be distinguished from each other. This could dramatically alter the landscape of biological sensing, and aid the development of practical biosensors by partially solving the problems of false positives and poor cross-sensitivities.

Detection in buffer

We have conducted initial studies on the detection of protein binding to the device architecture by using devices, and our results are displayed on Figure 5. Here more on what has been done, why is there such large noise (compared to Dai). Also something should be said about the importance of noise reduction.

Fig.5. a) Real time detection of streptavidin attachment of nanotubes, by monitoring the source-drain current as function of time, b) Change of the transistor characteristics after incubation with streptavidin. The change as observed is consistent with a charge transfer from the protein to the nanotube, (such charge transfer has also been seen in devices after buffer remova,seel A. Star et a1 Ref. 6). (M. Briman et a1, to be published) We have also examined the response time of the devices in the buffer environment and have found that the upper cutoff of the measurable time variations is approximately one microsecond. As discussed before (Refs 20-24), many of the important conformational changes occur at time scales significantly longer that this value, and consequently a variety of conformational fluctuations can be accessed by the electronic detection technique we propose to utilize. Sensor architecture development and fabrication Various sensor architectures will be fabricated, they rely on different sensing sites, and they also offer different opportunities for the electronic detection. In short, devices including an individual nanotube offer potentially single protein detection, while devices based on a (random) network, that includes a large number of single wall nanotubes offer a broader exploration of conformational changes on a (small) ensemble of biomolecules -with more clear application potential.It is however significantly more difficult to utilize his latter device architecture for single molecuyle detection. Fundamentally, for a construction that involves several nanotubes, and the electrical contacts, the current flows from the contact to one nanotube then to another tube and exciting through the other contact. Broadly speaking, sensing is determined by the largest resistance associated with the current path, and this can be the contact-nanotube interface, or, alternatively at the nanotube itself or at the nanotube-nanotube junction. Which of these dominate will depend on the sensing architecture that will be chosen. Devices with a single nanotube as the conducting channel. The company where the PI has spent a sabbatical, Nanomix Inc has developed methods for large-scale fabrication of devices where few nanotubes span the source and drain. Device imaging and electronic characterization of such devices can be used to identify devices where a single nanotube acts as conducting channel. Such devices will be used for real time detection of individual proteins and DNA oligomers. Nanotube network transistor devices. Although sensors with only a few -- and ideally with a single -nanotube sensing elements can be fabricated, initially the sensors will contain a random array of nanotubes, covering a relatively large surface area. Current flows along several conducting channels, and the presence of a bio-molecule blocks the nearby channels, thus increasing the overall resistance. The construction has several advantages, mainly it is fault tolerant: the destruction of one channel leaves other channels still open. The sensitivity is determined by a network that can be fine-tuned for specific applications. A change of the conducting path leads to the change of the resistance that can be detected. Such networks have been shown to be sensitive chemical sensors, and our objective is to explore their usefulness in bio-sensing. The reason for this approach is that with such configuration there is an increased likelihood for conformational changes occurring within a nanotube segment. We have developed a method of laying down such films employing porous alumina membranes as filters and measurement substrates. Microfluidic integration It is expected that the conductivity of the liquid plays an important role in device operation. We have found34that in liquids with low conductivity, such as cyclohexane, the device conductance is dominated by the nanotube channel, consequently the measured NTFET characteristic changes little compared to what is observed in air. With conductive liquids, such as de-ionized water three effects are important 6. First, the screening of the gate voltage prevents gating of the device, thus the NTFET operates in a zero gate condition, similar to a device coated with a conducting metal layer, such as palladium. Second, the liquid provides an additional conduction channel between the source and gate, leading to an increased source-drain current. In order to use the original chip for sensing in liquids, the wires and bond pads are covered with insulating epoxy. Only the region of the chips containing nanotubes and a distance of 0.5 mm around them was exposed to water, and the device is gated through the liquid. 6,35. We have also constructed a configuration that allows input for solution injection and the application of the gating electrodes. The container is surrounded by metal heat bath connected to temperature controller. The setup can be placed on a horizontally rotating plate for liquid mixing purpose. The configuration is different from arrangements in 36,37 and will allow the investigation of melting, and ligand-recepror binding at different temperatures. Research projects 1. DNA Electronic detection of DNA Our experiments focus on studies of melting and also duplex formation, with experiments on electronic detection proceeding hand-in-hand with optical experiments on the same species. Pre-melting conformational fluctuations of DNA. Both single strand and duplex DNA undergoes a variety of conformational changes, with important implications to biological processes. We will explore the fluctuations of DNA related to melting of the duplex, the separation of the strands upon increasing of temperature. We have found that in oligomers a so called Zipper model gives a first approximate description, but opening of the duplex by creating denaturation bubbles as also important. We will explore the melting process in DNA oligomers immobilized on the devices, and will investigate the conformational changes induced by external factors such as temperature, buffer PH, electric field and UV radiation. Temperature induced denaturing will be explored by measuring simultaneously the temperature dependent device characteristics and fluorescent signal, in both cases using identical oligomer immobilization methods. The initial experiments will be conducted on nanotube network devices onto which a large number of ssDNA oligomers will be immobilized, and this an ansable average will be detected. Duplex formation. Single strand DNA oligomers will be immobilized on the nanotube, and the resistance of the nanotube will be recorded simultaneously. Subsequently, a chip thus prepared will be immersed in a solution containing the complementary DNA strands. It is expected that when hybridization occurs, the resistance of the nanovire changes dueto the excess scattering of charge transfer due to the additional, charges DNA or RNA segment. These experiments will be conducted in conjunction with optical studies on the same oligomers. 2. Electronic detection of proteins Two lines of research is currently conducted. One involves the immobilization of various proteins onto non-functionalized devices, and the second will explore the details of the biotin-streptavidin ligand-receptor binding. Conformational changes of immobilized proteins. We are exploring the conformational changes of proteins, starting with bio-molecules for which earlier research established some dynamical properties. Protein- nanotube interactions and single protein detection. Electronic detection of ligand-receptor binding. In our initial studies we have detected ligand-receptor binding by using biotin-streptavtin binding as an example.biotin-streptavidin interaction will initially examined for several reasons.