## Slide 1: Dark Matter Searches by Liquid Xenon and Argon TPC XENON100, DarkSide50, XENON1Ton, MAX and XAX
University of California, Los Angeles
Department of Physics and Astronomy
arisaka@physics.ucla.edu
Katsushi Arisaka

## Slide 2: UCLA DM2010 Conference

## Slide 3: Talk Outline
Introduction
  What is Dark Matter? How to detect?
  CDMS vs. XENON
XENON100
  Detector System
  Current Status, Preliminary Results
QUPID
  Radiation Free Photon Detectors
Future Multi-ton Detectors
  XENON1T and DarkSide50
  MAX and XAX

## Slide 4: Introduction

## Slide 5
Seven Phases of Cosmic Evolution
14 billion years ago
Origin of
Particles
Origin of
Structure
Origin of
Life
Origin of
Consciousness

## Slide 6: Brain Universe
New York Times 8/21/2006
100 Billions Galaxies
100 Billions Neurons

## Slide 7
Formation of Structure in the Universe
Dark Matter is required!

## Slide 8: “Fossils” from the Earliest Universe
10-45sec
10-40
10-35
10-30
10-25
10-20
10-15
10-10
10-5
105 sec
1
1 year
103
106
109 year
Time
(sec)
Temp.
(oK)
1018
1015
1012
109
1PeV
1TeV
1GeV
1MeV
1KeV
1eV
1030
1025
1020
1015
1010
105
1
Energy (GeV)
10-3eV
Gravitational Wave
Neutralino
(Cold Dark Matter)
Relic Neutrino
(Hot Dark Matter)
GUT Particle
(Super Heavy Dark Matter)
Planck
EW
Now
GUT
The Big Bang!
Decoupling of “Fossils”

## Slide 9: What is Dark Matter?

## Slide 10: Target Mass Dependence of WIMP Cross Section
Si-28
Ne-20
10-44 cm2
Xe-132
Ge-73
Ar-40

## Slide 11: Detection Technique

## Slide 12: Double-Phase Noble Liquids

## Slide 13: XENON10 Detector

## Slide 14: XENON10 Results (2007)

## Slide 15: CDMS-II in Soudan

## Slide 16: CDMS-II New Results
2 event observed!
(0.8 surface BG
+ 0.1 neutron BG)
194 kg-days exposure = 4.4 kg x 139 day x 0.33 (eff.)

## Slide 17: 90% CL Limits of SI Cross Section
DAMA
CDMS-II
XENON10
ZEPLIN III

## Slide 18: 90% CL Limits of SI Cross Section
XENON100
DAMA
CDMS-II
XENON10
ZEPLIN III

## Slide 19: 90% CL Limits of SI Cross Section
Xe 1 ton
Ar 5 ton
XENON100
DAMA
CDMS-II
XENON10
MAX–G2
ZEPLIN III

## Slide 20: 90% CL Limits of SI Cross Section
Xe 1 ton
Xe 10 ton
Ar 5 ton
Ar 50 ton
XENON100
DAMA
CDMS-II
XENON10
ZEPLIN III
MAX–G2
MAX–G3

## Slide 21: Comparison of Xenon Detector Size
14cm
15cm
30cm
XENON100
170 kg
(30 kg)
XENON10
14 kg
(5.4 kg)
30 cm
20 cm
ZEPLIN-II
31 kg
(7.2 kg)
30 cm
G1
2007
2010
1 m
1 m
XENON1ton,
MAX-G2
2 ton (1 ton)
G2
1 m
2014
2007
2 m
XAX, MAX-G3
20 ton (10 ton)
G3
2018
2 m

## Slide 22: XENON100
60cm
30cm
XENON100
170 kg
(50 kg)
30 cm

## Slide 23: XENON100 Collaboration
Katsushi Arisaka
David Cline
Hanguo Wang
UCLA
DOE + NSF
NSF
NSF
Italy
Portugal
Switzerland
h

## Slide 24
WARP

## Slide 25: XENON100 Detector
170 kg
(30 kg)

## Slide 26: PMT Arrays
242 Hamamatsu R8520 PMTs 1"x1", optimized for response @ Xe scintillation light (175 nm)
Low radioactivity ( ~ <1 mBq/PMT)
Bottom Array
80 PMTs
~33% QE
Top Array
98 PMTs
~23% QE
Active Veto
64 PMTs
~23% QE

## Slide 27
XENON100 Detector
Ethan Brown

## Slide 28
XENON10 (2006 - 2007)
XENON100 (2008 ~ )
Notes: 28

## Slide 29
Pb
(20cm)
Pb
(20cm)
Poly
(20cm)
Cu
(5cm)
Poly
(20cm)
Cu
(5cm)

## Slide 30
Preamp
DAQ
Cooling
Tower

## Slide 31
A Typical Event
S1
S2

## Slide 32: Electron Life Time
from the bottom
(30 cm drift)
2010
2009

## Slide 33: AmBe Neutron Band
Ave.
Ave. – 3σ
Elastic DM
Inelastic DM

## Slide 34: Co60 Gamma Band
Ave.
Ave. – 3σ
Elastic DM
Inelastic DM
0.5%
S2/S1 rejection = 99.5%
(Same as XENON10)

## Slide 35: Status of XENON100
Purity of Xenon has achieved the design goal.
  Actual Goal
  Light Yield: 3.2 > 3 pe/keV
  Electron Drift Time: 300  > 300 μs
  Krypton 85: 50 - 100 < 100 ppt
  Radon: 1.1 ± 0.4 < 2 Bq/m3
Serious calibration runs under way.
  Neutrons: AmBe
  Surface gammas: Co-60, Cs-137
  Internal gammas : Kr-83m (9 keV, 32 keV)
Physics data taking started on January 15!

## Slide 36: Energy Spectrum of Real Data vs. MC
MC flux is multiplied by 0.75
30 kg
50 kg
Full target (63 kg)
XENON10 (5,4 kg, 0.6 DRU)
7 mDRU

## Slide 37: Z-R Distribution for Elastic Range before S2/S1 Cut
35 events
(7 mDRU)
30 kg
50 kg
Before S2/S1 Cut
(2 – 18 keVee)
10.6 days

## Slide 38: Z-R Distribution for Elastic Range after S2/S1 Cut
30 kg
50 kg
After S2/S1 Cut (99.5% Rejection)
(2 – 18 keVee)
0.17 BG expected
10.6 days

## Slide 39: LogS2/S1 Real Data for 0-50 KeVee
Ave.
Ave. – 3σ
0.17 BG expected
Elastic DM
Inelastic DM
35 events
(7 mDRU)
10.6 days

## Slide 40
Katsushi Arisaka, UCLA
40
Fiducial Mass
Live days
Efficiency
Effective Exposure
Relative exposure (over CDMS-II)‏
No. of Observed Events
No. of Gamma BG (before S2/S1 cut)‏
No. of Gamma BG (before S2/S1 cut)‏
S2/S1 Rejection Efficiency
No. of Expected Gamma BG (after S2/S1 cut)‏
kg
days
kg-days
Events
DRU
Events
Events
CDMS-II
4.4
139
0.317
194
1.00
2
0.80
XENON10
5.4
58.6
0.43
136
0.70
10
0.6
816
0.005
4.08
XENON100
(now)
30
10.6
0.4
127
0.65
0.007
35
0.005
0.17
XENON100
(Sept, 2010)
30
200
0.4
2400
12.4
?
0.007
700
0.005
3.5
Comparison of CDMS, XENON10 and XENON100

## Slide 41: 90% CL Limits of SI Cross Section
XENON100 (Sept, 2010)
DAMA
CDMS
XENON10
ZEPLIN III

## Slide 42: QUPID

## Slide 43
Underground or
Under high mountains
Detector
Water Tank
(Liquid Scintillator)
Where backgrounds come from?
Cosmic Rays
Radio Activities
(U, Th, K…)
Photon detectors are the major source of backgrounds.
XDNON100

## Slide 44: QUPID (QUartz Photon Intensifying Detector)
Quartz
Photo Cathode
(-6 kV)
APD (0 V)
Quartz
Quartz
Al coating
APD (0 V)
Photo Cathode
(-6 kV)
Made by Synthetic Silica only.
US Patent (No. 5374826) pending.

## Slide 45: Comparison of Low-radioactive Photon Detectors from Hamamatsu
QUPID
3 inch
R8520
1 inch
R8778
2 inch
XENON10
XENON100
LUX
(XMASS)
XENON1Ton
DarkSide50
MAX

## Slide 46: Spectrum of QUPIDs and Background (4 QUPIDs x 1 month data)
4 QUPIDs
No QUPID
11/16/12
Katsushi Arisaka, UCLA
46
 | 90% CL
238U | < 0.36 mBq
232Th | < 0.30 mBq
60Co | 0.12 ± 0.06 mBq
40K | < 1.96 mBq

## Slide 47: 1, 2 and 3 PE Distribution with 2m cable
2 PE
3 PE
1 PE
G = 800 × 200
= 160,000

## Slide 48: Summary of QUPID
Extremely low radioactivity: < 1 mBq
  < 0.1 neutron / year
  << 10 times lower than conventional low radioactive PMTs.
Large diameter: 3 inch
  6 inch is also under investigation.
Special Photocathode: Bialkali LT
  > 30 % QE at 170 – 450 nm
  Low resistivity even at Liquid Ar temperature (- 185 oC)
True photon counting.
  1, 2, 3… photoelectron peaks clearly visible.
  100% collection efficiency.
Simple HV supply.
  Common HV (-6 kV) for all QUPIDs
  Resister chain not necessary
The first successful operation in Liquid Xenon at UCLA!

## Slide 49
New 3” QUPID (Production Version)

## Slide 50
Cryogenic System at UCLA (Hanguo Wang’s Lab)
Artin Teymourian
Liquid Xe
Nitrogen

## Slide 51: Qupid Pictures
QUPID in the Cooling System

## Slide 52: Electron Bombardment Gain (QHA26)
25 oC
-100 oC
G = 800

## Slide 53: APD Gain and Leakage (QHA26)
-100 oC
-50 oC
25 oC
-100 oC
-50 oC
Gain
Leakage Current
25 oC
G = 200

## Slide 54
Cryogenic System at UCLA (Hanguo Wang’s Lab)
QUPID
in Liquid Xe

## Slide 55: The first Scintillating lights detected by QUPID from 57Co in Liquid Xenon
Threshold

## Slide 56: The first Scintillating lights detected by QUPID from 57Co in Liquid Xenon
2 PE
3 PE
1 PE
Threshold

## Slide 57: XENON1T
1 m
1 m
G2
XENON1ton,
MAX
2 ton (1 ton)
60cm
30cm
XENON100
170 kg
(50 kg)
30 cm

## Slide 58: XENON 1ton Structure
3” QUPID
(121 top,
121 bottom)
Titanium Vessel
(5 mm x 2)
Acrylic Spacer
(5 cm)
PTFE
(5 mm)

## Slide 59: XENON 1Ton
Xe 1.07 Ton
10 cm
Xe 2.12 ton

## Slide 60: XENON 1ton Top Corner

## Slide 61: XENON 1ton with Water Tank Shielding
Water Tank
(11 m ϕ x 11 m H)

## Slide 62: Gamma Background (After Multi-hit Cut and S2/S1 Cut)
2 DBD (1022 yrs)
WIMP (10-45 cm2)
pp Solar Neutrino
0 cm cut
Be7 Solar Neutrino
5 cm cut
10 cut

## Slide 63: Expected Backgrounds in XENON 1Ton (100 Year, Multi-hit Cut)
1.1 ton
0.07  / year
XENON100
1.1 ton
0.1 n / year
XENON100

## Slide 64: DarkSide 50

## Slide 65: DarkSide 50 with 19 + 19 QUPIDs
50 kg of 39Ar depleted Argon (33 kg fiducial)
19 + 19 = 38 QUPID
Liquid Scintillator Active Veto

## Slide 66: DarkSide Collaboration

## Slide 67: Properties of Noble Liqud
 | Unit | Neon | Argon | Xenon
Z |  | 10 | 18 | 54
A |  | 20 | 40 | ~132
Liquid Density | g/cc | 1.21 | 1.4 | 3.06
Energy Loss (dE/dX) | MeV/cm | 1.4 | 2.1 | 3.8
Radiation Length | cm | 24 | 14 | 2.8
Collision Length | cm | 80 | 80 | 34
Boiling Temperature | oK | 27.1 | 87.3 | 165
Scintillation Wavelength | nm | 85 | 125 | 175
Scintillation | photon/keV | 30 | 40 | 46
Ionization | e-/keV | 46 | 42 | 64
Decay time (Fast Component) | nsec | 19 | 7 | 4
Decay time (Slow Component) | nsec | 1500 | 1600 | 27
Isotope |  | No | 39Ar (1 Bq/kg) | 136Xe
Price | $ /ton | $90k | $2k | ~$1M
Single Phase Experiments |  | CLEAN | DEAP, CLEAN | XMASS
Double Phase Experiments |  |  | WARP, ArDM, DarkSide, MAX, XAX | ZEPLIN, LUX, XMASS, XENON, MAX, XAX

## Slide 68: Pulse Shaping Discrimination by Ar

## Slide 69
Princeton Prototype Plant for Depleted Argon:
Achieved 0.5 kg/day (depletion >25), 15 kg accumulated.

## Slide 70: MAX and XAX

## Slide 71: DUSEL ($750M project by NSF)

## Slide 72
XAX by UCLA Group (Aug, 2008)

## Slide 73: Original Concept of XAX
4 m
40Ar
70 ton
(50 ton)
WIMP
2 m
129/131Xe
12 ton
(6 ton)
WIMP (Spin odd)
Solar Neutrino
WIMP (Spin even)
Double Beta Decay
136Xe
7 ton
(4 ton)
1.2 m

## Slide 74: G2 and G3 facilities at DUSEL
 | G2 | G3
Sensitivity | < 10-46 cm2 | < 10-47 cm2
Target Mass | ~ 1 Ton | ~ 10 Ton
Cost | $15M - $20M | ~ $50M
defined by PASAG (Oct, 2009)

## Slide 75: Supports on both Xe and Ar

## Slide 76: MAX - Multi-ton Argon & Xenon
UMass Amherst, Arizona State University
Augustana College, Black Hills State University
Coimbra University, Columbia University
Fermilab, University of Houston, INAF, LNGS
MIT, University of Münster, University of Notre Dame
Princeton University, Rice University, Temple University
UCLA, Univesity of Virginia, Waseda University
University of Zürich
MAX Collaboration = XENON + DarkSide
Elena Aprile Christiano Galbiati

## Slide 77: 90% CL Limits of SI Cross Section
Xe 1 ton
Ar 5 ton
XENON100
DAMA
CDMS
XENON10
MAX–G2
ZEPLIN III

## Slide 78: 90% CL Limits of SI Cross Section
Xe 1 ton
Xe 10 ton
Ar 5 ton
Ar 50 ton
XENON100
DAMA
CDMS
XENON10
ZEPLIN III
MAX–G2
MAX–G3

## Slide 79
MAX – G3 Detector
Xe
20 ton
(10 ton)
2 m
4m
40Ar
70 ton
(50 ton)
6” QUPID x 3746
3” QUPID x 595 (Top)
6” QUPID x 825 (Side/Bottom)

## Slide 80
Xe 10 ton Detector Structure
Xe10 ton
(or Ar 5 ton)
20 cm
Xe 20 ton
(or Ar 10 ton)
2.1m
1.9m
Top: 3” QUPID x 595
Side: 6” QUPID x 672
Bottom: 6” QUPID x 163

## Slide 81
Xe 10 ton Top-Corner
3” QUPID
6” QUPID
Gas Xe (Ar)
Liquid Xe (Ar)
Mesh Wire

## Slide 82
MAX Shielding Structure
Water Tank
Liquid
Scinti
Water Tank
Xe 20 ton (10 ton)
40Ar 70 ton (50 ton)
18 m
8 m
Liquid
Scinti
Xe
Ar

## Slide 83
MAX Facility at DUSEL
Xe 20 ton
(10 ton)
Ar 70 ton
(50 ton)
Liquid Scintillator
(8 m ϕ x 8 m H )
Water Tank
(18 m ϕ x 18 m H)
Liquid Scintillator
(8 m ϕ x 8 m H )

## Slide 84: (SI) WIMP Energy Spectrum for Various Targets (Cross Section = 10-45cm2)
Xe-132
Ge-73
Ar-40
Si-28
Ne-20

## Slide 85: (SI) WIMP Energy Spectrum for LXe (Cross Section = 10-45cm2)
8 keVr
45 keVr
Xenon
200 GeV
50 GeV
100 GeV
1000 GeV
500 GeV
20 GeV

## Slide 86: (SI) WIMP Energy Spectrum for LAr (Cross Section = 10-45cm2)
20 GeV
200 GeV
50 GeV
100 GeV
1000 GeV
500 GeV
200 keVr
45 keVr
Argon
(w/ pulse shaping)

## Slide 87: 1-σ Error of WIMP Mass vs SI Cross Section (10 ton*year Xe and 50 ton*year Ar)
Argon
(42 events)
Xenon
(56 events)
G3
10-46 cm2
100 GeV
10-45
10-46
10-47
(40% eff.)
(80% eff.)

## Slide 88: 1-σ Error of WIMP Mass vs SI Cross Section (10 ton*year Xe and 50 ton*year Ar)
G3
50 GeV
100 GeV
200 GeV
500 GeV
10-45 cm2
Argon
Xenon

## Slide 89: (SI) WIMP Energy Spectrum for LXe (Cross Section = 10-45cm2)
20 GeV
200 GeV
50 GeV
100 GeV
1000 GeV
500 GeV
8 keVr
45 keVr
Xenon
Winter
Summer

## Slide 90: (SI) WIMP Energy Spectrum for LAr (Cross Section = 10-45cm2)
200 GeV
50 GeV
100 GeV
45 keVr
200 keVr
1000 GeV
500 GeV
Argon
(w/ pulse shaping)
Winter
Summer
20 GeV

## Slide 91: ±1σ Error of Annual Modulation Amplitude vs WIMP Mass (10 ton*year Xe and 50 ton*year Ar, Cross Section = 10-45cm2)
Argon
Xenon
10-45 cm2

## Slide 92: ±1σ Error of Annual Modulation Amplitude vs WIMP Mass (10 ton*year Xe and 50 ton*year Ar, Cross Section = 10-44cm2)
Argon
Xenon
10-44 cm2

## Slide 93: ±1σ Error of Annual Modulation Amplitude for various WIMP velocities (50 ton*year Ar, Cross Section = 10-44cm2)
10-44 cm2
Argon
170 km/s
195 km/s
220 km/s
245 km/s
270 km/s

## Slide 94
Expected Background from Gammas and pp Solar Neutrinos (100 Year, Multi-hit Cut, S2/S1 Cut)‏
02/25/10
Katsushi Arisaka, UCLA
94
2.3 ν /10 ton-year
(pp solar neutrino)
Xenon
10 ton
XENON100
5 × 10–8 DRU
’s from QUPID

## Slide 95: Xe 10 ton Neutron Background (100 Years)
0.81 n / year
Before Cuts
1/8
Multi Hit Cut
0.10 n / year
1/4
0.03 n / year
Liquid Scinti. Veto
Xenon
10 ton

## Slide 96: Ar 50 ton Neutron Background (100 Years)
42 n / year
2.1 n / year
0.39 n / year
1/20
1/6
Multi Hit Cut
Liquid Scinti. Veto
Before Cuts
Argon
50 ton

## Slide 97: Summary of MAX G2/G3 & XAX
 |  | MAX G2 |  | MAX G3 |  | XAX | 
 |  | Xenon | Argon | Xenon | Argon | 129/131Xe | 136Xe (80%)
Dimension |  |  |  |  |  |  | 
 | Detector Size | 1m x 1m | 2m x 2m | 2m x 2m | 4m x 4m | 2m x 2m | 
 | Total Mass | 2.2 ton | 10 ton | 20 ton | 70 ton | 13 ton | 7 ton
 | Fiducial Mass | 1.1 ton | 5 ton | 10 ton | 50 ton | 6 ton | 4 ton
QUPID |  |  |  |  |  |  | 
 | Top | 121 (3") | 595 (3") | 595 (3") | 661 (6") | 595 (3") | 
 | Side | 0 | 672 (6") | 672 (6") | 2423 (6") | 672 (6") | 
 | Bottom | 121 (3") | 163 (6") | 163 (6") | 661 (6") | 163 (6") | 
No.WIMP / year (10-45 cm2) |  |  |  |  |  |  | 
 | Mass = 20 GeV | 23 | – | 230 | – | 138 | 92
 | 50 GeV | 71 | 25 | 710 | 250 | 426 | 284
 | 100 GeV | 56 | 42 | 560 | 420 | 336 | 224
 | 200 GeV | 33 | 36 | 330 | 360 | 198 | 132
 | 500 GeV | 14 | 19 | 140 | 190 | 84 | 56
Backgrounds / year |  |  |  |  |  |  | 
 | Gammas | 0.07 | 0.00 | 0.01 | 0.00 | 0.07 | 0.01
 | Neutrons (w/o LS) | 0.10 | 0.78 | 0.10 | 2.1 | 0.10 | 0.00
 | Neutrons (w/ LS) | 0.03 | 0.10 | 0.03 | 0.39 | 0.03 | 0.00
Neutrinos / year |  |  |  |  |  |  | 
 | 0ν DBD (1027 yr) | 0.4 | – | 3.3 | – | – | 30
 | pp-solar | – | – | – | – | 2500 | –
 | Supernova (10 kpc) | 11 | 14 | 95 | 141 | 56 | 39

## Slide 98: Conclusions
XENON100 running extremely well.
  Already comparable sensitivity as XENON10 and CDMS-II in 10 days (30 kg fiducial).
  Background is 100 times lower than XENON10.
  By September, > 10 times larger exposure than CDMS-II.
QUPID successfully developed.
  The first signals in Liquid Xenon.
  Mass production (6 QUPID/day) almost ready.
Based on QUPUID, the future multi-ton Xe/Ar detectors designed and proposed.
  XENON 1ton and DarkSide 50 at Gran Sasso.
  MAX G3 (Xe 10 ton + Ar 50 ton) at DUSEL.

## Slide 99: 90% CL Limits of SI Cross Section
Xe 1 ton
Xe 10 ton
Ar 5 ton
Ar 50 ton
XENON100
DAMA
CDMS
XENON10
ZEPLIN III
MAX–G2
MAX–G3