## Slide 1: Direct WIMP Detection with Noble Liquids
University of California, Los Angeles
Department of Physics and Astronomy
arisaka@physics.ucla.edu
Katsushi Arisaka

## Slide 2: Talk Outline
Introduction
  Properties of Xenon & Argon
G1
  XENON100 - new results
  DarkSide 50
G2
  XENON 1 Ton
G3
  LZD and MAX
  Xenon 10 Ton + Argon 50 Ton

## Slide 3: Detection Technique
Double
Phase
Single
Phase

## Slide 4: Properties of Noble Liqud
 | Unit | Neon | Argon | Xenon
Z |  | 10 | 18 | 54
A |  | 20 | 40 | ~132
Liquid Density | g/cc | 1.21 | 1.4 | 3.06
Energy Loss (dE/dX) | MeV/cm | 1.4 | 2.1 | 3.8
Radiation Length | cm | 24 | 14 | 2.8
Collision Length | cm | 80 | 80 | 34
Boiling Temperature | oK | 27.1 | 87.3 | 165
Scintillation Wavelength | nm | 85 | 125 | 178
Scintillation | photon/keV | 30 | 40 | 46
Ionization | e-/keV | 46 | 42 | 64
Decay time (Fast Component) | nsec | 19 | 7 | 4
Decay time (Slow Component) | nsec | 1500 | 1600 | 26
Isotope |  | No | 39Ar (1 Bq/kg) | 136Xe
Price | $ /ton | $90k | ~$2k | ~$1M
Single Phase Experiments |  | CLEAN | DEAP, CLEAN | XMASS
Double Phase Experiments |  |  | WARP, ArDM, DarkSide, MAX | ZEPLIN, XENON, MAX LUX, LZD

## Slide 5: Target Mass Dependence of WIMP Cross Section
Si-28
Ne-20
10-44 cm2
Xe-132
Ge-73
Ar-40

## Slide 6: Double-Phase Noble Liquids

## Slide 7: XENON100 Detector
161 kg
(48 kg)

## Slide 8: PMT Arrays
242 Hamamatsu R8520 PMTs 1"x1", optimized for response @ Xe scintillation light (178 nm)
Low radioactivity ( ~ <1 mBq/PMT)
Bottom Array
80 PMTs
~33% QE
Top Array
98 PMTs
~23% QE
Active Veto
64 PMTs
~23% QE

## Slide 9
XENON100 Detector

## Slide 10
Pb
(20cm)
Pb
(20cm)
Poly
(20cm)
Cu
(5cm)
Poly
(20cm)
Cu
(5cm)

## Slide 11: Energy Spectrum of Real Data vs. MC
arXiv:1101.3866
85Kr
222Rn
136Xe
MC Total
Surface Backgrounds

## Slide 12: Log(S2/S1) vs. Energy
100.9 days, 48 kg
3 events
(1.8 ± 0.6 expected)
γ backgrounds
Neutron band
(Acceptace ~40%)
99.75% rejection for γ
8.4 keVnr
44.6 keVnr
-3 σ
S2 = 300 PE
S1 = 4 PE
S1 = 30 PE
arXiv:1104.2549

## Slide 13: Event distribution in z vs. R2
100.9 days, 8.4 – 44.6 keVnr
48 kg
3 events
(1.8 ± 0.6 expected)

## Slide 14: Log(S2/S1) vs. Energy
11 keVnr

## Slide 15: Single Scatter Nuclear Recoil Event Candidate
Top
Bottom
11 keVnr

## Slide 16: 90% CL Limits of SI Cross Section
arXiv:1104.2549
CMSSM

## Slide 17: Comparison of Xenon Detector Size
14cm
15cm
30cm
XENON100
161 kg
(48 kg)
XENON10
14 kg
(5.4 kg)
30 cm
20 cm
ZEPLIN-II
31 kg
(7.2 kg)
30 cm
G1
2007
2010
1 m
1 m
XENON 1ton
2.4 ton (1 ton)
G2
1 m
2014
2007
2 m
MAX, LZD
20 ton (10 ton)
G3
2019
2 m

## Slide 18: QUPID (QUartz Photon Intensifying Detector)
Photo Cathode
(-6 kV)
APD (0 V)
Quartz
Quartz
Al coating
APD (0 V)
Photo Cathode
(-6 kV)
Artin Teymourian’s talk

## Slide 19: XENON1T

## Slide 20: Expected Backgrounds in XENON 1Ton (100 Year, Multi-hit Cut)
1.1 ton
0.07  / year
XENON100
1.1 ton
0.1 n / year
XENON100

## Slide 21: DarkSide 50 kg  5 Ton
CTF Water Tank
Liquid
Scintillator
3” QUPID
(19 top + 19 bottom)
Depleted Ar
(50 kg)

## Slide 22
G2
G3
G1
CMSSM

## Slide 23: (SI) WIMP Energy Spectrum for LXe (Cross Section = 10-45cm2)
20 GeV
200 GeV
50 GeV
100 GeV
Xenon
8 keVr
45 keVr
1000 GeV
500 GeV

## Slide 24: (SI) WIMP Energy Spectrum for LAr (Cross Section = 10-45cm2)
20 GeV
200 GeV
50 GeV
100 GeV
Argon
30 keVr
200 keVr
1000 GeV
500 GeV

## Slide 25: 1-σ Error of WIMP Mass vs SI Cross Section (10 ton*year Xe and 50 ton*year Ar)
G3
50 GeV
100 GeV
200 GeV
500 GeV
10-46 cm2
10-45
10-46
10-47
10
50
10
50
Argon
Xenon

## Slide 26: 1-σ Error of WIMP Mass vs SI Cross Section (10 ton*year Xe and 50 ton*year Ar)
Argon
(42 events)
Xenon
(56 events)
G3
10-46 cm2
100 GeV
10-45
10-46
10-47
10
50
10
50

## Slide 27: LUX and LZD

## Slide 28
4m
MAX+LZD = G3 Detector
Xe
20 ton
(10 ton)
2 m
40Ar
70 ton
(50 ton)
3” QUPID x 595 (Top)
3” QUPID x 595 (Bottom)
3” QUPID x 2644 (Top)
3” QUPID x 2644 (Bottom)

## Slide 29
MAX+LZD = G3 Shielding Structure
Xe
20 ton
(10 ton)
18 m
Water Tank
Liquid
Scinti
Water Tank
18 m
8 m
40Ar
70 ton
(50 ton)
Liquid
Scinti

## Slide 30: G3 (MAX) at DUSEL
Xe
20 ton
(10 ton)
40Ar
70 ton
(50 ton)

## Slide 31: Projected Sensitivity
G3 = Xe (10T) + Ar (50T)
2010
Xe
Xe
Ar
Ar

## Slide 32: Conclusions
XENON100 new results announced.
  3 event observed (1.8 ± 0.6 events expected)
  < 7 x 10-45 cm2 (at 50 GeV)
  < 2 x 10-45 cm2 by the end of 2011 expected.
Future multi-ton Xe/Ar detectors designed and proposed.
  XENON 1T and DarkSide 50 / 5T at Gran Sasso.
  G3 = MAX + LZD (Xe 10T + Ar 50T) at DUSEL.