## Slide 1: Direct WIMP Detection by Noble Liquids : XENON100 and Beyond
University of California, Los Angeles
Department of Physics and Astronomy
arisaka@physics.ucla.edu
Katsushi Arisaka

## Slide 2: Talk Outline
Introduction
  Why Noble Liquid?
  Single Phase vs. Double Phase
  Xenon – XMASS, LUX, XENON100
  Argon – DEAP/CLEAN, WARP, DarkSide50
G1 : XENON100
  New Results
Future Directions
  G2 : XENON 1 Ton
  G3 : LZD and MAX (Xenon 10 Ton + Argon 50 Ton)
XAX and Neutrino Physics
  Solar neutrino
  Double beta decay
  Supernova neutrino

## Slide 3: Introduction

## Slide 4: Growth of Direct Detection Community

## Slide 5: What is Dark Matter?

## Slide 6: Detection Technique
Double
Phase
Single
Phase
(Ge, Si)
Gamma Ray
Neutron
WIMP

## Slide 7: Noble Gases

## Slide 8: Properties of Noble Liqud
 | Unit | Neon | Argon | Xenon
Z |  | 10 | 18 | 54
A |  | 20 | 40 | ~132
Liquid Density | g/cc | 1.21 | 1.4 | 3.06
Energy Loss (dE/dX) | MeV/cm | 1.4 | 2.1 | 3.8
Radiation Length | cm | 24 | 14 | 2.8
Collision Length | cm | 80 | 80 | 34
Boiling Temperature | oK | 27.1 | 87.3 | 165
Scintillation Wavelength | nm | 85 | 125 | 178
Scintillation | photon/keV | 30 | 40 | 46
Ionization | e-/keV | 46 | 42 | 64
Decay time (Fast Component) | nsec | 19 | 7 | 4
Decay time (Slow Component) | nsec | 1500 | 1600 | 26
Isotope |  | No | 39Ar (1 Bq/kg) | 136Xe
Price | $ /ton | $90k | ~$2k | ~$1M
Single Phase Experiments |  | CLEAN | DEAP/CLEAN | XMASS
Double Phase Experiments |  |  | WARP, ArDM, DarkSide, MAX | ZEPLIN, XENON, MAX LUX, LZD

## Slide 9: Target Mass Dependence of WIMP Cross Section
Si-28
Ne-20
10-44 cm2
Xe-132
Ge-73
Ar-40

## Slide 10: XMASS (Single Phase Xe)
100kg Prototype
（FV:30kg、30cm）
800kg Detector
（FV:100kg、80cm）
20ton Detector
（FV:10ton、2.5m）
Dark Matter
R&D
Solar neutrino
Dark Matter
completed
2011 〜
Future

## Slide 11
DEAP/CLEAN (Single Phase Ar/Ne)
360 kg Mini-CLEAN
3.6 ton DEAP/CLEAN

## Slide 12: Double-Phase Noble Liquids

## Slide 13: XENON100 (Double phase Xenon)
161 kg
(48 kg)

## Slide 14: LUX 350 kg (Double phase Xenon)
60 cm
350 kg
(100 kg)

## Slide 15: WARP 140 kg (Double Phase Argon)
60cm
140 kg
(100 kg)

## Slide 16: Pulse Shaping Discrimination by Ar (First WARP Results)
Gamma
Neutron
Gamma from 39Ar

## Slide 17: DarkSide 50 kg (Double phase Argon)
CTF Water Tank
Liquid
Scintillator
3” QUPID
(19 top + 19 bottom)
Depleted Ar
(50 kg)

## Slide 18: Comparison of G1 Experiments
Experiment Name | Location |  | Mass |  |  | Photon Detector |  |  |  | 
 |  | Target | Total | Fiducial | Phase | Type | Location | Size | Radioactivity | 
 |  |  | (kg) | (kg) |  |  |  | (inch) | (mBq /piece) | (mBq /cm2)
XENON100 | Gran Sasso | Xe | 162 | 48 | Double | R8520 | Top/Bot. | 1 | 1 | 0.2
XMASS | Kamioka | Xe | 800 | 100 | Single | R8778Hex | 4π | 2 | 5 | 0.2
LUX | DUSEL | Xe | 350 | 100 | Double | R8778 | Top/Bot. | 2 | 20 | 0.8
Mini-CLEAN | SNO | Ar | 360 | 100 | Single | 8" PMT | 4π | 8 | 500 | 1.5
WARP | Gran Sasso | Ar | 140 | 100 | Double | 3" PMT | Top | 3 | 200 | 4.4
DarkSide 50 | Gran Sasso | Ar | 60 | 50 | Double | 3” QUPID | Top/Bot. | 3 | 1 | 0.02

## Slide 19: Single Phase vs. Double Phase
 | Single Phase | Double Phase
HV for electron drift | Not required | Required (~1 kV/cm)
O2 / H2O impurity | Not critical | Critical
Energy threshold | 20 PE | 4 PE
Sensitivity for low mass WIMP | > 20 GeV | > 5 GeV
Position resolution | ~ 10 cm | ~ 2 mm
Gamma rejection by S2/S1 | No | Yes (> 99.5%)
Neutron rejection by Multi-hit cut | No | Yes

## Slide 20: Xenon vs. Argon
Xenon
  5 times more sensitive (per unit mass)
    due to A2 dependence.
  Expensive
    ~$1M / ton
  Limited by pp-chain solar neutrino
    ~0.2 event /ton/year
  Ideal for mass range of 10 – 100 GeV
    Spectrum is independent from mass
Argon
  Free from gamma background
    > 106 rejection by pulse shaping
  Inexpensive
  Ideal for mass range of 20 – 200 GeV
    Insensitive to low mass < 10 GeV

## Slide 21: XENON100

## Slide 22
WARP

## Slide 23: XENON100 Detector
161 kg
(48 kg)

## Slide 24: PMT Arrays
242 Hamamatsu R8520 PMTs 1"x1", optimized for response @ Xe scintillation light (178 nm)
Low radioactivity ( ~ <1 mBq/PMT)
Bottom Array
80 PMTs
~33% QE
Top Array
98 PMTs
~23% QE
Active Veto
64 PMTs
~23% QE

## Slide 25
XENON100 Detector

## Slide 26
Pb
(20cm)
Pb
(20cm)
Poly
(20cm)
Cu
(5cm)
Poly
(20cm)
Cu
(5cm)

## Slide 27
Preamp
DAQ
Cooling
Tower

## Slide 28: Energy Spectrum of Real Data vs. MC
arXiv:1101.3866
85Kr
222Rn
136Xe Double Beta Decay
MC Total
Surface Backgrounds

## Slide 29: Level of Backgrounds (before S2/S1 cut)
after fiducial cut
before fiducial cut

## Slide 30: New Leff vs. Energy
arXiv:1104.2587
Leff : Relative scintillation efficiency for nuclear recoils to 122 keV gamma rays (at zero electric field)

## Slide 31: Log(S2/S1) vs. Energy
100.9 days, 48 kg
3 events
(1.8 ± 0.6 expected)
γ backgrounds
Neutron band
(Acceptace 30 – 40%)
99.75% rejection for γ
8.4 keVnr
44.6 keVnr
-3 σ
S2 = 300 PE
S1 = 4 PE
S1 = 30 PE
arXiv:1104.2549

## Slide 32: Event distribution in z vs. R2
100.9 days, 8.4 – 44.6 keVnr
48 kg
3 events
(1.8 ± 0.6 expected)

## Slide 33: Log(S2/S1) vs. Energy
11 keVnr

## Slide 34: Single Scatter Nuclear Recoil Event Candidate
Top
Bottom
11 keVnr

## Slide 35: 90% CL Limits of SI Cross Section (April, 2011)
arXiv:1104.2549
CMSSM

## Slide 36: Inelastic Dark Matter
arXiv:1104.3121
CDMS
ZEPLIN III
XENON100
DAMA Allowed
δ = 120 keV

## Slide 37: Summary of XENON100
Purity of Xenon has achieved the design goal.
  Actual Goal
  Light Yield: 2.2 > 2 pe/keVee
  Electron Drift Time: 400 > 300 μs
  Krypton 85: 80 < 100 ppt
  Radon: 1.1 < 2 Bq/m3
100 days of data published.
  3 event observed (1.8 +- 0.6 events expected)
    Contaminated by 85Kr at ~ 700 ppt  1.1 events
  < 7 x 10-45 cm2 at 50 GeV arXiv:1104.2549
  Low mass (7-10 GeV) WIMP unlikely.
  Inelastic DM excluded. arXiv:1104.3121
Data taking continues.
  85Kr reduced to < 80 ppt
  < 2 x 10-45 cm2 by the end of 2011 expected.

## Slide 38: XENON100 data taking in 2011
March
April
May

## Slide 39: Future Directions

## Slide 40: DUSEL started in 2007 (~$1B project by NSF)

## Slide 41
XAX by UCLA Group (2008)
arXiv:0808.3968

## Slide 42: XAX (Xenon-Argon-Xenon)
14 m
12 m
Water Tank Veto
4 m
12 m
129/131Xe
12 ton
(6 ton)
40Ar
70 ton
(50 ton)
WIMP (Spin odd)
Solar Neutrino
WIMP (Spin even)
Double Beta Decay
WIMP (Spin even)
2 m
136Xe
7 ton
(4 ton)
1.2 m

## Slide 43
PASAG Report (2009)

## Slide 44: G2 and G3 facilities defined by PASAG (2009)
 | G1 | G2 | G3
Sensitivity | < 10-44 cm2 | < 10-46 cm2 | < 10-47 cm2
Target Mass | 10 – 100 kg | ~ 1 Ton | ~ 10 Ton
Cost | $1M – 5M | $10 – 20M | ~ $100M

## Slide 45: Supports on G2 and G3 Detectors

## Slide 46: Comparison of Xenon Detector Size
14cm
15cm
30cm
XENON100
161 kg
(48 kg)
XENON10
14 kg
(5.4 kg)
30 cm
20 cm
ZEPLIN-II
31 kg
(7.2 kg)
30 cm
G1
2007
2010
1 m
1 m
XENON 1ton
2.4 ton (1 ton)
G2
1 m
2014
2007
2 m
MAX, LZD, XAX
20 ton (10 ton)
G3
2019
2 m

## Slide 47
G2
G3
G1
CMSSM

## Slide 48
Underground or
Under high mountains
Detector
Water Tank
(Liquid Scintillator)
Where backgrounds come from?
Cosmic Rays
Radio Activities
(U, Th, K…)
Photon detectors are the major source of backgrounds.
XDNON100

## Slide 49: QUPID (QUartz Photon Intensifying Detector)
Photo Cathode
(-6 kV)
APD (0 V)
Quartz
Quartz
Al coating
APD (0 V)
Photo Cathode
(-6 kV)
arXiv:1103.3689

## Slide 50
New 3” QUPID (Production Version)

## Slide 51: Comparison of Low-radioactive Photon Detectors from Hamamatsu
QUPID
3 inch
R8520
1 inch
R8778
2 inch
XENON10
XENON100
LUX
(XMASS)
DarkSide50
XENON1Ton
MAX, XAX

## Slide 52: QE of two types of QUPID
Chart: Wavelength [nm]
Xenon (178 nm)
Argon + TPB (420 nm)

## Slide 53: 1, 2 and 3 PE Distribution with 2m cable
2 PE
3 PE
1 PE

## Slide 54: 7 QUPID Array on Base Plate at UCLA

## Slide 55: XENON1T (G2)

## Slide 56: Expected Backgrounds in XENON 1Ton (100 Year, Multi-hit Cut)
1.1 ton
0.07  / year
XENON100
1.1 ton
0.1 n / year
XENON100

## Slide 57
4m
MAX Detector (G3)
Xe
20 ton
(10 ton)
2 m
40Ar
70 ton
(50 ton)
3” QUPID x 595 (Top)
3” QUPID x 595 (Bottom)
3” QUPID x 2644 (Top)
3” QUPID x 2644 (Bottom)

## Slide 58
MAX (G3) Shielding Structure
Xe
20 ton
(10 ton)
18 m
Water Tank
Liquid
Scinti
Water Tank
18 m
8 m
40Ar
70 ton
(50 ton)
Liquid
Scinti

## Slide 59: MAX at DUSEL
Xe
20 ton
(10 ton)
40Ar
70 ton
(50 ton)

## Slide 60: US Dark Matter Programs
G3 = Xe (10T) + Ar (50T)
2010
Xe
Xe
Ar
Ar

## Slide 61: Xe 10 ton Neutron Background (100 Years)
0.81 n / year
Before Cuts
1/8
Multi Hit Cut
0.10 n / year
1/4
0.03 n / year
Liquid Scinti. Veto
Xenon
10 ton

## Slide 62: Ar 50 ton Neutron Background (100 Years)
42 n / year
2.1 n / year
0.39 n / year
1/20
1/6
Multi Hit Cut
Liquid Scinti. Veto
Before Cuts
Argon
50 ton

## Slide 63: (SI) WIMP Energy Spectrum for LXe (Cross Section = 10-45cm2)
8 keVr
45 keVr
Xenon
200 GeV
50 GeV
100 GeV
1000 GeV
500 GeV
20 GeV

## Slide 64: (SI) WIMP Energy Spectrum for LAr (Cross Section = 10-45cm2)
20 GeV
200 GeV
50 GeV
100 GeV
1000 GeV
500 GeV
200 keVr
40 keVr
Argon
(w/ pulse shaping)

## Slide 65: 1-σ Error of WIMP Mass vs SI Cross Section (10 ton*year Xe and 50 ton*year Ar)
G3
50 GeV
100 GeV
200 GeV
500 GeV
10-45 cm2
Argon
Xenon

## Slide 66: 1-σ Error of WIMP Mass vs SI Cross Section (10 ton*year Xe and 50 ton*year Ar)
G3
50 GeV
100 GeV
200 GeV
500 GeV
10-45
10-46
10-47
10
50
10
50
Argon
Xenon
10-46 cm2

## Slide 67: 1-σ Error of WIMP Mass vs SI Cross Section (10 ton*year Xe and 50 ton*year Ar)
Argon
(42 events)
Xenon
(56 events)
G3
100 GeV
10-45
10-46
10-47
10
50
10
50
10-46 cm2

## Slide 68: 1-σ Error of WIMP Mass vs SI Cross Section (10 ton*year Xe and 50 ton*year Ar)
100 GeV
Argon
(4.2 events)
Xenon
(5.6 events)
G3
10-46
10-47
10-48
10-47 cm2
10
50
10
50

## Slide 69: Neutrino Physics

## Slide 70
Energy Spectrum (Natural Xe)
Be7 Solar
B8 Solar
2 DBD (1022 yrs)
pp Solar
0 DBD (1027 yrs)
100 GeV WIMP (10-44 cm2)
arXiv:0808.3968

## Slide 71: XAX (Xenon-Argon-Xenon)
14 m
12 m
Water Tank Veto
4 m
12 m
129/131Xe
12 ton
(6 ton)
40Ar
70 ton
(50 ton)
WIMP (Spin odd)
Solar Neutrino
WIMP (Spin even)
Double Beta Decay
WIMP (Spin even)
2 m
136Xe
7 ton
(4 ton)
1.2 m
arXiv:0808.3968

## Slide 72: Neutrino-less Double Beta Decay

## Slide 73
2 DBD (1022 yrs)
0 DBD (1027 yrs)
0 cm
10 cm
30 cm
20 cm
B8 Solar Neutrino
40 cm
50 cm
136Xe Double Beta Decay and Gamma Background
(1 mBq / QUPID, 2m Xenon Detector)

## Slide 74: Double Beta Decay Experiments
EXO 1Ton
EXO200
NEMO3 (Mo)
NEMO3
(Se)
Mass (kg)
No. of Backgrounds (/year)
Cuoricino
GERDA I
GERDA II
GERDA III
Super-NEMO (Se)
CUORE I
CUORE II
CUORE III
COBRA
CANDLES III
EXO 1Ton
(Ba tag)
1025 yrs
1026 yrs
1027 yrs
1028 yrs
XAX (Enriched)
XAX (Natural)
XENON1T

## Slide 75: Solar Neutrino Detection

## Slide 76: Solar Neutrino (by XMASS group)
M. Nakahata

## Slide 77: Sular Neutrino Detection
M. Yamashita

## Slide 78: Solar Neutrino Study by XMASS Group
M. Nakahata

## Slide 79: Summary

## Slide 80
G2
G3
G1
CMSSM

## Slide 81: Detection of Cosmic Radiation
XENON10
IMB
Kamiokande
AMANDA
Super-K
HiRes
AGASA
XENON1T
MAX / XAX
LBNE (Water)
JEM-EUSO
Future
CDMS-II
1990
2000
2010
Dark Matter
Neutrino
Cosmic Ray
Larger Volume
Lower Threshold
XENON100
ICECUBE
Pierre-Auger
Ongoing
Past
2020

## Slide 82: XAX vs. Super-K
XAX
Liquid Xenon (20 ton)
Energy Threshold = 5 MeV
20” PMT x 11,200
Energy Threshold = 5 keV
3” QUPID x 4,000
Super-K
Pure Water (50,000 ton)
2 m
40 m

## Slide 83: Conclusions
XENON100 new results announced.
  3 event observed (1.8 ± 0.6 events expected)
  < 7 x 10-45 cm2 (at 50 GeV WIMP mass)
  < 2 x 10-45 cm2 by the end of 2011 expected
Future multi-ton Xe/Ar detectors designed and proposed.
  G2 : XENON 1T and DarkSide 50 / 5T at Gran Sasso.
  G3 : MAX + LZD (Xe 10T + Ar 50T) at DUSEL
XAX is an ultimate general purpose detector with ~ 5 keV threshold.
  Double beta decay
  Solar (pp-chain) and supernova neutrinos